RICE Hydro, Inc.

3500 Arrowhead Drive

# Carson City,  NV  89706

800-245-4777

Installation and Assembly Instructions

3B-Pressured Accessory Tank

Assembly Parts Included:

(1) 20 gallon tank in mounting bracket with hose assembly

(1) ¾” Inlet assembly garden hose swivel

(1) 1” x 90 degree Hosebarb Connector

(1) Hose clamp

Mounting tank bracket to Pump Frame:

Mount the 3B-Pressured tank assembly bracket on the outside of pump frame, aligning the wide angle feet with the pre-drilled frame holes.  When installing with a Wheel and Handle kit, place handle holes to the inside of the pump frame.  Use (4) 5/16 x 1 & ¾” Hex Bolts with washers to secure in place.

Use pipe sealant or Teflon tape on all fitting connections to ensure a tight seal.

Connecting tank outlet to Pump inlet piping:

Suction feeding hose from pump to tank, is pre-assembled and connected to the bottom of the tank.  Screw the 1” x 90-degree hosebarb provided into the inlet piping of pump.  Slide hose with clamp over inlet hosebarb and tighten, to secure in place.

Tank Inlet Hookup:

Connect nipple and hose swivel assembly to the tank inlet port on the upper side of tank where the pressure valve and float assembly are already internally attached.

Revised 02/23/05